## Slide 1: Project Proposal - BUTTON HOOK
Team 7
Pietro Sainaghi
Shubham Kiran Wani
Rodrigo Uribe
Huajing Zhao

## Slide 2: Motivation & Background
Robots have been used to dress physically impaired individuals
Issue: robots can only put the clothes on, but cannot buttoning them
We will use a buttonhook with tactile-driven control to perform the robot-assistive garment fastening task
  Tactile sensors at robotic fingers provides slip detection
  Tooltip and cloth fabrics/buttons has dynamic contacts
  Need to distinguish effects at finger-tool and tool-environment interfaces
Team 7 - Button Hook
Project Proposal

## Slide 3: Functionality & Task
The tooltip can be modeled as an elastic beam
Simulate the hooktip dynamics
  Lateral pulling and angular twisting motions
  In contact with cloth fabrics and rigid buttons
A novel contribution to tool-manipulation: finger-tool v.s. tool-environment interactions
  Model the relative motions and dynamic contact of tooltip
  Assist the tactile-driven slip and shear force detection
Team 7 - Button Hook
Project Proposal
Notes: The tooltip of button hook is of slender and compliant structure that can be modeled as an fixed-ended elastic beam

## Slide 4: Project Overview
Simulate using 3-d rod model
  Structure is slender and long enough for assumption to be valid
  Tension, Torsion, Bending
Use ‘zeros’ of torsional springs to create hook shape
Simulate deformation and forces:
  Going through button hole
  Hooking button
  Alignment twisting motion
  Unhooking button
Team 7 - Button Hook
Project Proposal

## Slide 5: Objectives
Construct a simulation of the button hook.
Verify that we accurately depict the current design.
Adjust the parameters for optimal performance.
  Material Selection (Material Properties)
  Geometry Design (Curvature, Rod Geometry)
Team 7 - Button Hook
Project Proposal

## Slide 6: Planned Deliverables
Define button hook as rod object
Test interactions with basic forces
Define boundary conditions for various interactions
  Go through button hole
  Hook Button
  Twist motion to align button
  Unhook button
Simulate interactions
Construct motion sequence
Compare different geometries and material properties
Team 7 - Button Hook
Project Proposal

## Slide 7: Thank you! - Any questions?